## Slide 1
Quiz
A technician is testing an AC power supply that produces a sinusoidal output. Using a true-RMS multimeter, the reading is 17.0 VAC at 60 Hz. The technician needs to verify whether certain resistors can safely handle this voltage.
(a) What is the peak voltage of this supply?
(b) What is the peak-to-peak voltage?
(c) The technician has a 330 Ω resistor rated at 0.5 W. Calculate the power it would dissipate if connected across the supply, and state whether the resistor can safely handle it.
(d) The technician wants to limit the power dissipated to exactly 0.25 W. What resistance value should be used?
*** End of Quiz ***