## Slide 1
Quiz
A student observes a sinusoidal waveform on an oscilloscope. The waveform swings between +21.2 V and −21.2 V at 50 Hz. The student needs to select a resistor to place across this signal for a lab experiment.
(a) What is the peak-to-peak voltage of this waveform?
(b) Determine the RMS voltage.
(c) Calculate the power that a 470 Ω resistor would dissipate in this circuit.
(d) The student has a 180 Ω resistor rated at 0.5 W. Calculate the power it would dissipate if connected across this signal, and state whether the resistor can safely handle it.
*** End of Quiz ***